## Slide 1
Decoder
aka Codec and DCD
Stephane Gros

## Slide 2: Introduction
Why a decoder? Offload the host
Third party IP from Allegro DVT
Features: AVC, HEVC, JPG, post-processing, up to 4K

## Slide 3: Block diagram – IP level
DCD wrapper (dcd_p)
Allegro DVT IP
Credit: Stefan Mach

## Slide 4: Block diagram – System integration
Read/Write frame buffers (DDR, L2)
MCU code + data (DDR, L2)
IP configuration (APU)
Credit: Stefan Mach

## Slide 5: Verification strategy
Strategy
  The IP is already verified by the vendor
  What we want to verify
    Integration of RAMs and other technology components  block level
    Integration to the rest of the system  system level
    Performances  system level
Tests:
  Pre-built: traces provided by Allegro DVT for a first level of validation (block level only)
  Baremetal
    Traces generated with Allegro DVT’s validation flow and streams
    Converted to C for system level verification or directly run on the block level testbench
  Linux: tests using the linux driver provided by Allegro DVT
Coverage
  Testplan
  Toggle coverage on the interface
  Performances
Source: Allegro DVT

## Slide 6: Block level testbench
alg_amba_sram
alg_amba_ctrl
load
load
Executes
Source: Allegro DVT
Source: Allegro DVT
DIFF
decoder_scoreboard
AXI MCU
AXI Core0
AXI Core1
Based on the testbench delivered by Allegro  plug and play with their validation flow
Modifications
  Adaptation to our env (vsim support, pass/fail condition)
  Comparison done by the testbench
  UVM friendly
  Added a scoreboard for debug
read
read

## Slide 7: System level testbench
compile
Baremetal driver
Credit: Max Wipfi
Load .elf

## Slide 8: Thank you!
Any questions?

## Slide 9: Useful link
Architecture specification: https://doc.axelera.ai/prod/europa/latest/europa_architecture/blocks/dcd/dcd_block_spec/
Verification document: https://doc.axelera.ai/prod/europa/latest/europa_verification/dcd_verification_document/#verification-strategy
Recording: Decoder verification presentation-20240801_103259-Meeting Recording.mp4